## Slide 1: ENGI 301 Voice-Controlled Car Proposal
10/04/202
Jae Hyen Kim

## Slide 2: Background Information
What is being proposed?
  Pictures
  Links to existing projects / libraries
What improvements / additions over existing project

## Slide 3: Background Information
My project proposal is for a voice-controlled car
The idea is to essentially create a “remote” controlled car but in place of the remote will be a speech-to-text api that will detect when someone says certain keyword commands (such as forward, right, left, backward, stop) to move
  The api/microphone used for text-to-speech could be on the PocketBeagle/car itself or potentially on a webserver so that you can utilize your phone or similar device as a microphone instead
  Useful library: https://pypi.org/project/SpeechRecognition/
There is an existing project for creating a remote-controlled car using the PocketBeagle controlled via Bluetooth (https://www.hackster.io/christina-mezmur/remote-control-car-w-pocketbeagle-and-arduino-f2b006)
  The main change to this existing project would be to convert from a Bluetooth controlled model to a text-to-speech controlled model

## Slide 4: System Block Diagram
PocketBeagle
Texas Instruments Dual H-Bridge motor drivers L293D (x2)
Wi-Fi Dongle
USB1
GPIO
Driver Inputs
Motors (x4)
Driver Outputs
Input
Motor Power
Motor Power
Driver Power
Vout

## Slide 5: Power Block Diagram
PocketBeagle
Texas Instruments Dual H-Bridge motor drivers L293D (x2)
Wi-Fi Dongle
USB1 (+3.3V)
GPIO
Driver Inputs
Motors (x4)
Driver Outputs
(1 A)
Input
Motor Power (4.5 V – 36 V)
Motor Power (3V)
Driver Power (5V)
Vout
(3.3V)
Will need step up
Will need step down

## Slide 6: Components / Budget
Component | Need to Buy | Cost
Spark-fun Multi-Chassis Basic 4WD Kit | Y | $34.95
Texas Instruments Dual H-Bridge motor drivers L293D (x2) | Y | $2.80
Wi-fi Dongle* | N | 
4x AA Batteries | N | 
* No specific wi-fi dongle specified because I think you said you had some available