## Slide 1: ENGI 301 Voice-Controlled Car Proposal
10/04/202
Jae Hyen Kim

## Slide 2: Background Information
My project proposal is for a voice-controlled car
The idea is to essentially create a “remote” controlled car but in place of the remote will be a speech-to-text api that will detect when someone says certain keyword commands (such as forward, right, left, backward, stop) to move
  The api/microphone used for text-to-speech could be on the PocketBeagle/car itself
  Useful library: https://pypi.org/project/SpeechRecognition/
There is an existing project for creating a remote-controlled car using the PocketBeagle controlled via Bluetooth (https://www.hackster.io/christina-mezmur/remote-control-car-w-pocketbeagle-and-arduino-f2b006)
  The main change to this existing project would be to convert from a Bluetooth controlled model to a text-to-speech controlled model

## Slide 3: Supported Voice Commands
Forward
  Move the car in the “forward” direction a specified distance (all wheels spin at same speed in same direction)
Backward
  Move the car in the “backward” direction a specified distance (all wheels spin at same speed in same direction)
Right
  Turn the car in the “right” direction 90° (left side wheels spin faster than right side wheels)
Left
  Turn the car in the “left” direction 90° (right side wheels spin faster than left side wheels)
Stop
  Make sure all wheels are not turning

## Slide 4: System Block Diagram
PocketBeagle
Texas Instruments Dual H-Bridge motor drivers L293D (x2)
Audio Adapter
USB1
GPIO
Driver Inputs
Motors (x4)
Driver Outputs
Input
Motor Power
Motor Power
Driver Power
Vout
Microphone